## Slide 1: WP6 – Photofission station
ENEA, the 25th of January 2023
Adrien SARI

## Slide 2: Introduction
The photofission reaction
  Energy threshold ≈ 6 MeV for most actinides (U-235, U-238, Pu-239, etc.)
  Deployed using a linear electron accelerator (“linac”)
  Adapted to the characterization of radioactive waste packages with large volumes and/or concrete matrices

## Slide 3: Introduction
The photofission reaction

## Slide 4: Objectives
WP6 is focused on developments around a LINAC based platform. Two main purposes are related to this WP:
  Optimize a stationary non-destructive measurement cell, based on a linac in order to characterize large concrete nuclear waste packages and be able to declassify some of them, especially those identified as legacy waste
  Adapt photofission measurements to obtain a relocatable measurement cell, based on a LINAC and deployable on different D&D sites

## Slide 5: Theoretical description of the system
Three main building blocks
  A linear electron accelerator (linac)
  A radioactive waste package to be characterized
  A detection system for photofission particles
    Delayed neutrons (usually based on He-3 filled-gas proportional counters)
    Delayed gamma-rays (BGO, plastic scintillators, HPGe)

## Slide 6: Theoretical description of the system
The Linatron® M9 housed at the SAPHIR platform (CEA Paris-Saclay)
  Pulses of either 6 or 9 MeV electrons
  High-energy photons produced by Bremsstrahlung in the conversion target
Cooling system
Touchscreen controle console
Modulator
X-ray head and RF unit

## Slide 7: Theoretical description of the system
Two types of setups studied
  Stationary system
    9 MeV linac
    Study based on the Linatron M9 linac which is housed at the SAPHIR platform  Electron energy available: 9 MeV
   Monte Carlo simulation study + experiments
  Mobile system
    7 MeV linac
    Study based on the Linatron M9 linac which is housed at the SAPHIR platform  Electron energy shifted “virtually” by simulation: 7 MeV
   Monte Carlo simulation exclusively

## Slide 8: Theoretical description of the system
Detection blocks
  Five He-3 filled-gas proportional counters (150NH100 model)
  Block made of HDPE and surrounded by cadmium
View from the side
Global view

## Slide 9: Work done
Monte Carlo simulation study
  Optimization of the interrogative photon beam delivered by the linac
  Assessment of the measurement performance with a 7 MeV linac
  Conceptual design and shielding for a mobile photofission system (WP6/WP2)
  Study of additional configurations (WP6/WP8)
Experimental work
  Photofission measurement methodology and uncertainty assessment (WP6/WP8)
  Experiments carried out at the SAPHIR platform with a 9 MeV linac (CEA Paris-Saclay)

## Slide 10: Monte Carlo simulation study
Use of two Monte Carlo codes
  MCNP6.2
  PHITS v.3.16
   Gain critical mind on simulation results
Objectives of this simulation study
  Characterization and optimization of the photon beam delivered by a 7 or 9 MeV linac
  Assessment of the performances of the photofission technique at 7 MeV
  Assessment of the shielding for the conceptual design of a mobile linac-based system

## Slide 11: Monte Carlo simulation study
Neutron energy spectrum: various target materials (PHITS)
Neutron angular distribution: various target materials (PHITS)

## Slide 12: Monte Carlo simulation study
Photofission measurements at 7 MeV linac: a new challenge
  Energy threshold of the photofission reactions: 6 MeV for most actinides
  Three nuclear databases compared (ENDF, JENDL, TENDL)
   Photofission cross-sections at 7 MeV is almost >3 times lower than at 9 MeV
   Discrepancies between the nuclear databases => differences in results between PHITS and MCNP6
U-235
Pu-239

## Slide 13: Monte Carlo simulation study
Characterization of the photon beam of a 7 MeV linac
  PHITS versus MCNP6
  Example obtained for the energy spectra
   Similar discrepancies were observed for the linac operated at 9 MeV
   They primarily come from the differences in the nuclear databases (ENDF for MCNP ; JENDL for PHITS)

## Slide 14: Monte Carlo simulation study (WP6/WP2)
Conceptual design of the mobile system: shielding around a 7 MeV linac
   75 cm of heavy concrete required on the front wall
   50 cm of shielding of heavy concrete required on the other sides
10 cm
20 cm
30cm
40cm
50cm
Heavy concrete (density of 4.64 g/cm3) - various thicknesses

## Slide 15: Monte Carlo simulation study (WP6/WP8)
Study of several additional cases
  Measurement assumptions
    Irradiation of 10 min
    Electron peak current: 100 mA
    Pulse duration: 2.5 µs
    Electron energy: 7 MeV
    Detection block with five 3He tubes (150NH100)
    Delayed neutrons counted in interpulse model
View of the MCNP6 simulation model

## Slide 16: Measurement methodology
Uncertainty assessment in collaboration with WP8
Photofission measurement hot spots
Quantification U+Pu
Photofission tomography
Optional technique used in « expertise mode »
U <> Pu
Identification
Scanning along the vertical axis
2b
1
3
2a
Actinide mass
4

## Slide 17: Measurement methodology
Uncertainty assessment (for illustration: “step 2a” versus “step 2b”)

## Slide 18: Experimental work

## Slide 19: Experimental work

## Slide 20: Experimental work

## Slide 21: Experimental work

## Slide 22: Additional Monte Carlo simulations
Asessment of virtual cases at 7 MeV
  220 L-drum and 3 matrices: concrete, PVC, steel
  Simulation of delayed neutron counts obtained in interpulse mode at 100 Hz for various irradiation times
Signals obtained at 7 MeV are about 15 times lower than at 9 MeV
An irradiation time about an hour would be realistic for an industrial application

## Slide 23: Experimental work
Canberra 7820 – 7821 modules
  2 NIM modules (not supported anymore by Canberra)
    7820: ADS amplifier for signal amplification and spectra
    7821: HV module
    Configuration of each module through one cable
    Non user-friendly user interface

## Slide 24: Experimental work
Canberra 7820 amplifier
  Limited gain selection  10, 100 or 1000
  Limited bandwidth  ~20 MHz (20 ns rise time)
  1 input channel  bundling of several detectors with connectors
  BCC circuit  second stage amplification with bandwidth reduction
  Limited resolution on the discrimination circuit  40 mV
Timing application
  Output of 7820 linked to an MCA (Canberra MULTIPORT II)
  Only 4096 bins
    Poor bining in macro-pulse mode (duration of several minutes)
    Necessity to provide a trigger for interpulse mode
    Signal is summed between each pulse  loss of data
    Interpulse and macropulse need to be setup sequentially
Proprietary user-interface  post-treatment needs to be done separately

## Slide 25: Experimental work
New digital readout electronics developed by CEA List
  4 channels each equipped with:
    ADC 250 MHz 14 bits
    Current preamplifier with adjustable gain
  Embedded Programmable Logic Features (FPGA)
    Oscilloscope
    Counter
Timing application
  Home-made user interface  can be customized for future applications
  1 ms binning with continuous data saving
    Transition from interpulse to macropulse modes without interruption
    No data is lost in interpulse or between the two modes

## Slide 26: Summary
Monte Carlo simulation study
  Use of two Monte Carlo codes (MCNP6 and PHITS)
  Optimization of the photon interrogative beam of the linac
  POC of photofission measurements with a 7 MeV mobile system (WP6/WP2)
  Several additional calculations for uncertainty assessment (WP6/WP8)
Experimental work at the SAPHIR platform (CEA Paris-Saclay)
  Tests on 220 liter-nuclear waste mock-up drums with a 9 MeV stationary system
  Development by CEA List of new digital readout electronics and significant enhancement compared to traditional 7820-7821 Canberra modules
  Photofission measurements integrated in the DigiWaste ToolBox (WP6/WP9)

## Slide 27: Dissemination
International conferences
  Two oral presentations
  Two poster presentations
Articles
  Two peer-reviewed papers
  One conference proceedings

## Slide 28: Acknowledgements
The SAPHIR team
  Iaroslav MELESHENKOVSKII
  Aly ELAYEB
  Roberto DE STEFANO
The electronics team
  Yoann MOLINE
  Alexandre DABAT-BLONDEAU
The SAPHIR team for the MICADO project