## Slide 1: WP2: Virtual cases WP8: Combination of measurements and uncertainty assessment
Final Demonstration, 25 January 2023
Eric Breuil (ORANO) & An Bielen (SCK CEN)
Notes: 30 minutes

## Slide 2: Outline
WP2: Virtual cases
WP8: Uncertainty assessment
  General
  Approach
    Bayesian inference
    True and surrogate models
  Results
    VC1
    VC3

## Slide 3: WP2 Virtual Cases
3 virtual cases defined :
  Case n°1 : 120L drum containing 5 bags of decontamined wipes
  Case n°2 : 120L drum containing metal wastes
  Case n°3 : 210L drum containing 6 compacted waste discs
3 MCNP files
To be used by the partners for some developments in the design phasis, e.g. to test algorithms.

## Slide 4: Virtual case n°1 : 120L drum containing 5 bags of decontaminated wipes
Radioactive waste :
      5 Bags of wet decontaminated wipes (C3H6)
      a activity only : 9,48 GBq (0,4 g of Pu) in the drum
      Spectrum : Industrial Pu
      Each bag has a specific :
        Composition and density
        Proportion of water
        a activity
Package interest :
  Realistic packages in the nuclear industry
  Package characteristics were established to study the impact of the different measurement methods
  Possibility of carrying out an inactive mock-up drum with neutron sources (existing methodology)
  Impact of hydrogen in the package, in particular on the neutron characterization methods
Bag n°1
Bag n°2
Bag n°3
Bag n°4
Bag n°5

## Slide 5: Virtual case n°2 : 120L drum containing metal waste
Radioactive waste :
  A valve in the bottom of the drum with 0.68 g of Pu retention (0.77 g of PuO2)
  About fifty pipes in the rest of the drum 0.12 g of Pu distributed inside all the pipes
  Spectrum : Very Old Weapon Grade
  a activity : : 7.956 GBq in the valve and 1.404 GBq in the pipes
Package interest :
  Realistic packages in the nuclear industry
  Package containing significant Pu retention (fissile material) at the bottom of the package, which could be underestimated (risk of non-compliance)
  Contribution of MICADO compared to classical characterization methods
Set of pipes
Valve
Valve
Residual Pu

## Slide 6: Virtual case n°3 : 210L drum containing 6 compacted waste discs
Radioactive waste :
      6 compacted waste discs in a concrete matrix :
    2 metallic waste discs
    3 technological waste discs
    1 PVC waste disc
  Each disc has a specific :
        Composition and density
        Height
        Spectrum (a and/or bg spectrum)
        Activity level
      Radiological characteristics :
        Total a activity : 2.84 GBq (150 mg of Pu)
        Total b activity : 11.41 GBq
Package interest :
  Realistic packages in the nuclear industry
  Package containing a et bg spectrum (with fissile material)
  Contribution of MICADO compared to classical characterization methods (for each primary drum before compaction)
Longitudinal section
of a package
6 compacted waste discs in a concrete matrix

## Slide 7: WP8: Uncertainty assessment
Bag n°1
Bag n°2
Bag n°3
Bag n°4
Bag n°5
Impact of H in the package
Easily modelled
High density
2 different vectors
Gamma spectrometry SGS
Virtual case 1
Passive & active neutron coincidence (PNCC & ANCC)
Gamma spectrometry SGS
Passive neutron coincidence (PNCC)
Virtual case 3
Notes: The criteria for each measurement technique to select two out of three cases comprised the added value, the feasibility (e.g. duration calculations and detection limits) and the work load and calculation time that should stay realistic.
Since VC2 is the most difficult case for performing neutron measurements, as well as for detecting gamma rays, this case has not been considered.
When there is a question about LINAC: Why not LINAC? Many delays due to covid. Besides that, there were some technical issues. So there was no possibility anymore to perform the calculations. And SCK CEN has no experience with calculations for LINAC unlike the techniques of gamma spectrometry and neutron (Has CEA something to add?)

## Slide 8: WP8: Uncertainty assessment
Roadmap
  Identification of all sources of uncertainties for each measurement technique
  Quantification of all sources of uncertainties
    MCNP simulations based
    Focus on 2 virtual cases
  Propagate into final uncertainty
    Individual measurement techniques
    Combination of measurement techniques
Approach
  Bayesian inference
  Surrogate modeling
Notes: Flowchart -> how these uncertainties propagate into a final uncertainty on the inventory for a given waste package.
Measured values -> The actual observed values from the measurements, but also the observed waste package properties (volume, mass)
Input values -> are related to the measurement setup itself
Propagated values -> intermediate results
Final result = activity concentration
Approach is further explained in the following slides.

## Slide 9: Approach: Bayesian inference - MCMC
input
final result
+ Any distribution
- Multiple observations inform about the same thing
- No check for data-model consistency
MC
measured
gross counts
efficiencies
activities
activities
efficiencies
simulated
gross counts
measured
gross counts
MCMC
measured
bkg counts
bkg counts
prior distribution
posterior distribution
data misfit/likelihood
+ Updating of prior beliefs according to Bayes theorem
+ Any distribution
+ Multiple observations inform about the same thing
+ Verification if forward model is consistent with observations
Notes: Standard error propagation = first order Taylor expansion (standard rules for error propagation)
MC -> Monte Carlo = more advances but does not allow improving the result using multiple observations
MCMC -> Markov Chain Monte Carlo = Bayesian approach -> step towards machine learning

## Slide 10: Approach: From true to surrogate model
“True” MCNP model
+ simulate result
Example:
Neutron measurement technique VC1
Surrogate MCNP model + performing simulations
Notes: Drum is modeled as 1 mm thickness stainless steel
5 sub volumes modeled, each with 2 matrices and 2 densities

## Slide 11: Approach: From true to surrogate model
“True” MCNP model + simulate result
Example:
Gamma spectrometry
VC3
Surrogate MCNP model + performing simulations
Notes: Drum is modeled as 1 mm thickness of stainless steel.
The concrete is modeled only on the sides of the compacted drums (and not between – above and below) the discs.
Each compacted disc is modeled with an envelope of 1mm stainless steel.

## Slide 12
Measurement Techniques
Gamma spectrometry
Passive coincidence neutron counting
Active neutron interrogation
Meta data
Measurement data
WP8
Data assessment
(MICADO data analysis pipeline)
Connection
(WP9)
DigiWaste Platform (WP9)

## Slide 13
no prior information is available
prior information is available
Results VC1: Individual radionuclides
Notes: Each nuclide has a different color and the points denote the “true” values.
no prior information about the Pu vector (or anything else) is available
  We jointly infer a total Pu mass together with a vector for the 5 Pu nuclides) and nuclide to total Pu ratios (“scaling factors”) for Am-241 and other Pu-related nuclides (if any). So in both cases, the total Pu mass can vary between 0 g and 1 g (uniform prior distribution between 0 g and 1 g). The inferred vector is assigned a flat (Dirichlet) prior, which means that the inferred vector components can take any value between 0 % and 100% (under the constraint that they sum up to 100% - this is guaranteed by the use of a Dirichlet prior distribution).
  Adding PNCC to SGS nicely allow for resolving the Pu-242 distribution, which is totally uncertain otherwise. Adding ANCC to SGS also helps but to a (much) lesser extent.
prior information about the Pu vector is available and used to guide the inference
  The inferred vector is assigned a (Dirichlet) prior distribution that favors the values of the prior vector estimate. In practice, that means that the inferred vector is allowed to differ by a few percent from the prior vector estimate,
  It is seen that all nuclides but the non gamma-emitting Pu-242 nuclide are well resolved by SGS (called Gamma in the figure). Pu-242 is still relatively well constrained by its prior distribution though. Then when adding PNCC to SGS, the Pu-242 posterior distribution becomes well resolved as well. Regarding ANCC, it doesn’t bring much here.

## Slide 14: Results VC1: Total Pu mass
Notes: Summary
Total Pu mass
Gamma resolves good, but more accuracy when PNCC and ANCC are added

## Slide 15
Results VC1: Sub-volumes surrogate model
Gamma & PNCC (no prior information)
Notes: This picture is to show that more detailed information can be obtained, this per segment for the individual radionuclides.
Most of the Pu mass is situated at the bottom of the drum.

## Slide 16
no prior information is available
prior information is available
Results VC3: Individual radionuclides

## Slide 17
Results VC3: Total Pu mass

## Slide 18: Conclusions
Results
  VC1
    Combining techniques results in more accurate estimates
    Much better for “legacy” waste
  VC3:
    Underestimation of activity concentration due to
      Complex structure (composition & radionuclide vectors)
      Linear approach is used
    Gamma spectrometry: small uncertainty for gamma-emitting radionuclides
    PNCC: relatively accurate for determining total Pu mass when prior information is available
Bayesian inference and surrogate model approach
  Well suited for quantifying uncertainty in radiological characterization of radioactive waste
  Decrease of the measurement uncertainty when combining measurement techniques
  Success depends on the accuracy of the set of reference efficiencies (simulations)
Future
  Explore further how to mitigate possible errors and bias (nonlinear surrogate models)
  Various cases will be worked out
  Implementation of approach in industrial installations
Notes: KPI
Chance + micado

## Slide 20
Pu
Average density: 0.42
Bags with wet wipes
Known
Isotopic composition
Activity distribution
Density distribution
Chemical composition
Pu-239/Pu-240 4.2
12
9
17
8
6
0.53
0.36
0.38
0.52
0.32
9
9
12
8
8.5
True model
Surrogate models
Surrogate models
4.2
Isotopic composition
Activity distribution
Density distribution
Chemical composition
6
17
0.32
0.52
8
12